DIRECTION

NOTICE:

PLS READ CAREFULLY BEFORE INSTALLATION AND PRESERVE IT WELL. MUST BE INSTALLED AND ASSEMBLED BY A QUALIFIED ELECTRICIAN.

PARAMETER:

| Model | BL919WU1 / BL919WD1 / BL919H300 / BL919H1000 / BL919H1850 |
| --- | --- |
| Rate Voltage | AC 220-240V~ 50/60Hz |
| Rate wattage | BL919WU1 / BL919WD1 / BL919H300 / BL919H1000 MAX. 60W BL919H1850 MAX 3x60W |
| Safeguard grade | CLASS I IP44 |
| Lampholder | E27 |

INSTALLATION DIRECTION:

BEFORE ATTEMPING TO INSTALL UNITS, ENSURE POWER IS OFF, AND PLEASE PAY ATTENTION TO FOLLOWING SETPS:

Installation of wall lamp:

1: Turn off the main power.

2: First install plastic expansion piece in wall. Insert two fixed screws in plastic plate.

3: Fix the plastic plate on the wall with plastic expansion piece and self-tapping screws.

4: Connect supply leads with terminal brown (L) to brown, blue (N) to blue and greenish-yellow (〨) to greenish-yellow.

5: Fix the lantern to the base with screw.

6: Insert the new bulb in lamp holder, bulb must not exceed wattage specified on fixture label. Fix the lamp cover with screw.

7: Turn on the main power.

Installation of ceiling lamp:

1: Turn off the main power.

2：Insert the new bulb in lamp holder, bulb must not exceed wattage specified on fixture label. Fix the lamp cover with screw.

3: Install plastic expansion piece in the ceiling. Insert two fixed screws in plastic plate.

4: Fix the plastic plate on the plastic expansion piece with self-tapping screws.

5: Connect supply leads with terminal brown (L) to brown, blue (N) to blue and greenish-yellow (〨) to greenish-yellow.

6: Fix the lantern to the base with screw.

7: Turn on the main power.

Installation of post lamp:

1: Turn off the main power.

2: First install plastic expansion piece in ground. Insert two fixed screws in plastic plate.

3: Connect supply leads with terminal brown (L) to brown, blue (N) to blue and greenish-yellow (〨) to greenish-yellow.

4: Fix the lamp base on the ground with self-tapping screws.

6: Insert the new bulb in lamp holder, bulb must not exceed wattage specified on fixture label. Fix the lamp cover with screw.

7: Turn on the main power.